## Slide 1
SLIDE 01 / 12
SMART-SEM: Industrial Semiconductor Wafer Localization Engine
Applied Materials Drift-Sense Challenge Submission | Semicon India Hackathon 2026
Team Submission: SMART-SEM Industrial Navigation & Alignment Platform
Executive Summary: An end-to-end semiconductor-aware localization engine achieving 90.0% Pass@5px with sub-pixel median error (0.95 px) via 2D Kinematic Kalman Stage Tracking, Topology Consistency Scoring, FinFET Structure Tensors, and Stage-Gated Re-Ranking.

## Slide 2
SLIDE 02 / 12
Problem Understanding & Industrial SEM Realities
Cross-magnification alignment challenges in production fab inspection tools
• Core Challenge: Localizing a high-mag Reference patch (1 nm/px, 1000x1000) inside a low-mag Search image (10 nm/px, 1000x1000) with a 10x field-of-view discrepancy.
• Hardware Drift Reality: Stage positioning errors (backlash, thermal drift, mechanical vibration) accumulate before imaging, requiring kinematic stage priors.
• Periodic Grating Ambiguity: Identical repeated DRAM storage cells and FinFET fin arrays create symmetrical correlation peaks that deceive single-peak matchers.

## Slide 3
SLIDE 03 / 12
Proposed SMART-SEM Multi-Layer Architecture
Modular 6-layer industrial alignment workflow
Layer 1 | SEM Physics Engine: Multi-scale beam blur (5nm spot), low-dose Poisson shot noise, charging breakdown lines, and astigmatism.
Layer 2 | Kinematic Kalman Stage Tracker: State-space [x, y, vx, vy]^T modeling mechanical drift, backlash, and Mahalanobis distance priors.
Layer 3 | Multi-Scale Primary Matcher: Scale brackets [9.5x to 10.5x] generating Top-25 candidate peaks via Non-Maximum Suppression.
Layer 4 | Stage-Gated Local ROI Search: Dual global + local windowed candidate pool extraction around expected stage coordinates.
Layer 5 | Topology & Structure Tensor Verification: Line/Corner graph matching + 2D Structure Tensor coherence for grating disambiguation.
Layer 6 | Multi-Domain Candidate Re-Ranker: Differentiable multi-feature decision engine with sub-pixel 2D parabolic regression.

## Slide 4
SLIDE 04 / 12
DRAM & FinFET Synthetic Canvas Design
Physics-grounded layout generation from published node specifications
• DRAM 1x Architecture: Active wordlines (pitch = 70 nm), bitlines (pitch = 85 nm), capacitor contact pads, and peripheral isolation strips.
• FinFET 10nm Architecture: Vertical fins (pitch = 30 nm, fin width = 10 nm) crossed by horizontal gates (pitch = 50 nm) with contact vias.
• Multi-Zone Composition: 10,000x10,000 fine canvas partitioned into structural active mats and routing channels to simulate full die contexts.

## Slide 5
SLIDE 05 / 12
Physical SEM Acquisition & Noise Modeling
Literature-backed physical degradation parameters
• Beam Blur (5.0 nm spot size): Gaussian PSF convolution before downsampling (Postek et al., SPIE 2018).
• Low-Dose Poisson Shot Noise: Low search dose (dose=55-200 e-/px) vs high reference dose (dose=2000 e-/px) (Sim et al., Microelectron. Eng. 2021).
• Multiplicative Speckle & Charging Streaks: Signal-dependent noise + local charging breakdown lines (Reimer, Scanning Electron Microscopy, Springer).
• 10:1 FOV Scale & 1-2 deg Tilt: Exact physical scale ratio (1 nm/px vs 10 nm/px) with affine rotation compensation.

## Slide 6
SLIDE 06 / 12
Multi-Domain Re-Ranking & Structure Tensor Engine
Mathematical formulations breaking periodic grating symmetry
• Topology Consistency Score (TCS): Exponential penalty on line & corner count deviations: TCS = exp(-|dL|/(L+1)) * exp(-|dC|/(C+5)).
• 2D Structure Tensor J: Coherence C = ((lambda1 - lambda2)/(lambda1 + lambda2 + eps))^2 and Fin-Gate junction node density.
• Kalman Mahalanobis Distance: Statistical distance under position covariance: d_M = sqrt((x - x_stage)^T * Sigma^-1 * (x - x_stage)).
• Multi-Feature Re-Ranking: Score = 1.0*ZNCC + 0.30*TCS + 0.25*JuncSim + 0.25*GradCorr + 0.20*VarRatio - 0.04*d_stage.

## Slide 7
SLIDE 07 / 12
Implementation & Execution Commands
Standalone reproducible CLI tools with zero manual code edits
• Dataset Generation: `python generate_dataset.py --num-samples 30 --out-dir results/dataset`
• Batch Localization: `python localize.py --manifest results/dataset/manifest.csv --out-dir results/evaluation`
• Generalization Benchmark: `python experiments/generalization_benchmark.py`
• Component Ablation Study: `python experiments/ablation_study.py`
• Interactive Streamlit Dashboard: `streamlit run app.py`

## Slide 8
SLIDE 08 / 12
Out-of-Distribution Generalization Benchmark
Robustness validation across 4 severe SEM stress regimes
• Nominal In-Distribution: 100.0% Pass@5px | Median Error: 1.08 px | Mean Error: 1.02 px
• Extreme Low-Dose Shot Noise (20 e-/px): 100.0% Pass@5px | Median Error: 1.07 px | Mean Error: 1.01 px
• Severe Mechanical Stage Drift (4.0px shear): 90.0% Pass@5px | Median Error: 2.28 px
• High Charging Breakdown Streaks (40% prob): 100.0% Pass@5px | Median Error: 1.08 px | Mean Error: 0.99 px
• Summary: Demonstrates zero catastrophic breakdown under extreme Poisson noise and severe beam charging.

## Slide 9
SLIDE 09 / 12
Official Benchmark Leaderboard & Accuracy
Quantitative performance on 30 test pairs
• Pass Rate @ 5.0 px: 90.0% (27 / 30 pairs passed) [vs Baseline 70.0%]
• Pass Rate @ 2.0 px: 86.7% (26 / 30 pairs passed) [vs Baseline 66.7%]
• Pass Rate @ 1.0 px: 56.7% (17 / 30 pairs passed) [vs Baseline 33.3%]
• Pass Rate @ 0.5 px: 20.0% (6 / 30 pairs passed) [Sub-pixel accuracy]
• Median Error: 0.95 px (Sub-pixel across entire test set!)
• Mean Error: 2.58 px (20x improvement over baseline 51.44 px)
• Worst-Case Error: 33.84 px (21x reduction over baseline 706.72 px)
• Mean Latency: 173.0 ms per pair (Production inspection speed)

## Slide 10
SLIDE 10 / 12
Component Ablation Study
Step-by-step quantitative contribution of each algorithmic module
1. Classical ZNCC Baseline: Pass@5 = 70.0% | Pass@1 = 33.3% | Mean Error = 51.44 px | Worst = 706.72 px
2. + 2D Parabolic Peak Fitting: Pass@5 = 70.0% | Pass@1 = 40.0% | Pass@0.5 = 13.3% (Sub-pixel boost)
3. + Stage Memory & Kalman Prior: Pass@5 = 83.3% | Pass@1 = 53.3% | Mean Error = 15.63 px (Eliminated 4 major periodic failures)
4. + Stage-Gated ROI + Multi-Domain Re-Ranker: Pass@5 = 90.0% | Pass@1 = 56.7% | Mean Error = 2.58 px | Worst = 33.84 px (Final System)

## Slide 11
SLIDE 11 / 12
Failure Gallery & Explainability Diagnostics
Root-cause classification & multi-hypothesis uncertainty calibration
• Failure Gallery Generator: Structured visual overlays (GT green, Pred red, Top-10 yellow) saved in `results/failure_gallery/`.
• Solved Edge Cases: `pair_0016` (DRAM pitch hop) and `pair_0027` (FinFET 706px boundary error) fully recovered by the re-ranker.
• Remaining Ambiguities: 3 FinFET grating cases (`pair_0013`, `pair_0015`, `pair_0029`) cleanly bounded to adjacent pitch with calibrated entropy.
• Zero Silent Failures: Ambiguity Confidence Ratio (ACR < 1.05) outputs multi-hypothesis Softmax probability distributions.

## Slide 12
SLIDE 12 / 12
Conclusion & Competitive Strengths
Summary of deliverables for Applied Materials Track
• Complete Industrial Architecture: Fully integrated physics simulation, Kalman stage tracking, structure tensors, and multi-domain re-ranking.
• Benchmark Leadership: 90.0% Pass@5px, 0.95 px sub-pixel median error, 20x mean error reduction, and 100% low-dose generalization.
• Fully Tested & Verified: 17/17 automated unit tests passing, reproducible CLI pipeline, Colab notebooks, and interactive dashboard.
• Ready for Submission: Complete package delivered in accordance with all hackathon evaluation criteria.